## Slide 1
Velocity (Eulerian approach)
vx = gka/ [cosh [k(y+h)]/cosh(kh)]cos[k(xcos+zsin )- t]
vy = gka/ [sinh [k(y+h)]/cosh(kh)]sin[k(xcos+zsin )- t]
In the next figure we show the behaviour from deep water to sahallow water

## Slide 3
Acceleration
ax = vx,t+ [(vx2 +vy2)/ 2],x
ay = vy,t+ [(vx2 +vy2)/ 2],y
That assume the following espression on deep water and on shallow water
ax=(gka) exp(ky) ax~(gka)
ay= (gka)exp(ky) ay= (gka) ks

## Slide 5: The Stream Function is ,y = ,x - ,x = ,y = ga/[sinh (ks)/cos(kh)]cos and consequenlty the current line are described by ga/[sinh (ks)/cos(kh)]cos = costante

## Slide 7: To evaluate on a dynamic approach it is necessary to define the pressure that it is obtained adopting the Bernoulli eq. In irrotanionl flow, as p/ + gy + [(,x)2+ [(,y)2]/2 + ,t=0 that at the I ordine became p/ + gy + ,t=0 and introducing the axix s is p= -g(s-h) + g[cosh(ks)/cosh(kh)] That shows the hydrostatic componente and the dynamic component that it is proportional to the response factor Kp= cosh(ks)/cosh(kh) See next Figure 10

## Slide 9: Total energy of sea state = Kinetical en. + Potential en. Ep()=  gydy only over the mean sea water level Ec()=   [(v,x)2+ (v,y)2/2 ]dy only under the mean sea water level over a period equale to 2, Ep=Ec= gH2/8 on deep water and on shallow water conditions

## Slide 10: Instantaneous, local energy flux due to wave motion and related to a vertical section perpendicular to the direction of propagation and extending from the bottom to the free surface expressed by Ef = [pd+ [(v,x)2+ (v,y)2/2 ] v,xdy introducing some approximation and semplifications we obtain Ef=Ecg on deep water and in shallow water became Ef=( ga2/2)c/2 Ef ~ =( ga2/2)c

## Slide 12: The superposition of wave trains with equal amplitude but wave numbers and angular frequencies that differ from each other by small amounts k and  gives rise to wave groups that propagate with a particular speed referred to as group velocity
cg=c/2 [1+2kh/sinh(2kh)]
Where c= phase velocity
c=[(g/k) tanh(kh)]½
Then on deep water and in shallow water became
cg=c/2 cg=c